## Slide 1
同化变量
（固定的）
背景场模式变量
观测变量
控制变量
C2M
Bkgd
M2O
实现模块的分离
变分函数和导数计算
直接利用复合函数关系不再根据变量名字判断
where is the Laplacian operator, is background error covariance, and is the observation error covariance

## Slide 2: Multigrid design
MOTOR is designed to allow users to use different methods or schemes at each multigrid level.
Thus, each multigrid level may have different C2M, such as coarse grid shallow water, hydrostatic over grids coarser than 10 km, and non-hydrostatic at finer grids. C2M must be designed for a single grid, not multigrid.
A higher level of module should set different C2Ms, such as an application module.

## Slide 3
Application
Multigrid
MPI
Minimization
C2M
C2M
C2M
3DVar
4DVar
dyCore
Z-Grid
C-Grid
Shallow water
Hydro-static
Nonhydro-
static
RHS

## Slide 4
The current implementation of background is in model space
A 4DVar has its model constraint: with initial condition
Based on the current technology of reducing strong constrained minimization to an unconstrained one, we treat
all strong constraints as a mapping from control variables to assimilation variables. That is, for data assimilation
variables, we need to construct a mapping in C2M module,

## Slide 5
Processor 1
Processor 3
Observation
Cell center
1
2
3
For thinning, the observation needs
1,2 and 3 cells to interpolate the BK
to Obs. At processor 1, 3 is a halo.
When thinning process runs on
processor 1, it puts a weight on cell
3. However, processor 3 cannot see
This observation.

## Slide 6: Directory dependency: Developers should pay attention to these dependencies to avoid conflicts
MOTOR-PS
Public utilities
Geometry
External systems
Parallel computing
MOTOR-DA
MOTOR-QC
MOTOR-PP
Applications
Unit Tests
Static
Users level
Developer level
Architect level
MOTOR-DA:
1. Control to model state depends on NWP
2. DA depends on obs operators
3. Ensemble covariance depends on PP